CTS TMT—CON OCCUPATIONAL HAZARD ASSESSMENT AND CONTROL

Note 1: Alberta’s Occupational Health and Safety Code (OH&S Code) provides specific compliance requirements. This document is meant as a summary or checklists to assist staff comply with the legislation or applicable school jurisdiction administrative policies and regulations.

Note 2: The employee is required to conduct a pre-job hazard assessment before commencing work.

Note 3: This is a general worksite hazard assessment. Depending on the school/instructional area/specific courses taught, some incidents/hazards may or may not be present.

| RISK ANALYSIS (A x B x C = DEGREE OF RISK) |
| --- |
| A Frequency of Exposure to Hazard | B Incident/Hazard Probability | C Potential Consequence | Degree of Risk | Risk Classification |
| 1 = Less than once a month 2 = At least once a month 3 = At least once a week 4 = One or more times daily | 1 = Not likely 2 = Remote: not likely by once every 5–20 yrs 3 = Occasional: likely to happen once every 1–5 yrs 4 = Probable: expected to happen one or more times/year | 1 = Negligible (no injury, first aid) 2 = Marginal (medical aid, minor injury or illness) 3 = Critical (lost time injury, temp. disability) 4 = Catastrophic (serious injury or illness) | 1–11 12–31 32–64 | L – Low M – Medium H – High |

| POTENTIAL HAZARD | POTENTIAL HAZARD DESCRIPTION | RISK ANALYSIS (A x B x C = Degree of Risk) | SUMMARY OF EXISTING CONTROLS |
| --- | --- | --- | --- |
|  |  |  | ENGINEERING | ADMINISTRATIVE Alberta’s Occupational Health and Safety Codes (OH&S Code) applicable school jurisdiction administrative policies and regulations | PERSONAL PROTECTIVE EQUIPMENT (PPE) Personal Protective Equipment (PPE) appropriate for the work is both worn and CSA certified/approved where required. | CONTROL IN PLACE YES/NO |
| Biological Exposure | body fluid exposure from injuries | Biological 4 x 4 x 1 = 16 Medium | sink for handwashing first aid kit and supplies | Use universal precautions. Ensure that personnel are trained in first aid. Post emergency procedures. Identify and establish sanitary and safe housekeeping practices. Establish handwashing practices. | protective gloves (latex or nitrile disposable gloves) safety glasses, goggles | ( YES ( NO |
| Chemical Exposure | contact with finishes (paints) and solvents that may be splashed into eyes, absorbed into the skin, or inhaled. | Chemical 4 x 4 x 2 = 32 High | local and general ventilation | Ensure WHMIS training is available. Provide up-to-date MSDS. Follow safe handling and storage information on labels or MSDS. Ensure regular cleaning and maintenance of ventilation system. | protective gloves eye protection apron | ( YES ( NO |
|  | respiratory hazard and potential allergic response to dust and particulate from processing of wood materials, and toxic woods (e.g., cedar) | Chemical 4 x 4 x 2 = 32 High | local and general ventilation dust collection | Identify and establish sanitary and safe housekeeping practices. Secure and use the least toxic and harmful substance for the students and the environment. | approved half respirators for toxic dust | ( YES ( NO |
|  | dust from wood as a flammable particulate | Chemical 4 x 4 x 2 = 32 High | dust collection systems | Identify and establish sanitary and safe housekeeping practices. Avoid machining wood with nails/staples that could cause sparks. Avoid using the dust collection system to clean up metallic debris, such as nails and staples, as they may cause sparks a source of ignition. Do not use compressed air to clean clothing or machinery. Follow the manufacturer’s instructions for operation, maintenance, and repair of tools and equipment. | n/a | ( YES ( NO |
|  | flammable finishes (spray and brushed) | Chemical 4 x 4 x 2 = 32 High | flammable finishes applied in finishing room where there is local and general exhaust ventilation flammable finishes spray applied in room with intrinsically safe electric equipment flammable liquids dispensed in area with local exhaust ventilation flammable liquids stored in non-flammable storage cabinets | Ensure WHMIS training is available. Provide up-to-date MSDS. Follow safe handling and storage information on labels or MSDS. Dispose of flammable waste in appropriate waste containers, which are cleaned out at regular intervals and not allowed to accumulate. | n/a | ( YES ( NO |
| Ergonomic Exposure | lifting or moving heavy and awkward materials | Ergonomic 4 x 4 x 2 = 32 High | n/a | Perform a hazard assessment, considering the weight, size, shape, and number of times and manner in which the load will be moved. | n/a | ( YES ( NO |
| Physical Exposure | confined space (e.g., entering dust collector to check condition of bags) | Physical 4 x 4 x 3 = 48 High | n/a | Maintain and follow the manufacturer’s manuals for the operation, maintenance, and repair of equipment. Provide and document ongoing safety education and training, including mandatory equipment and tool orientation. Follow procedures for working in confined spaces. | hard hats safety glasses safety footwear (construction sites) hearing protection approved respirator | ( YES ( NO |
|  | shocks and electrocution (e.g., if equipment is not locked out) | Physical 4 x 4 x 3 = 48 High | n/a | Maintain and follow the manufacturer’s manuals for the operation, maintenance, and repair of equipment. Provide and document ongoing safety education and training, including mandatory equipment and tool orientation. | n/a | ( YES ( NO |
|  | contact with moving/flying objects (e.g., wood being cut with a table saw, materials being shaped by lathe) | Physical 4 x 4 x 3 = 48 High | equipment guards anti-kickback devices | Provide and document ongoing safety education and training, including mandatory equipment and tool orientation. Provide initial training to include a thorough review of hazards and accidents associated with the job. | n/a | ( YES ( NO |
|  | contact with moving parts that can cut, pinch, entangle | Physical 4 x 4 x 3 = 48 High | equipment guards | Provide and document ongoing safety education and training, including mandatory equipment and tool orientation. Provide initial training to include a thorough review of hazards and accidents associated with the job. Secure loose clothing, tie back long hair, and remove jewellery. | n/a | ( YES ( NO |
|  | contact with other persons within the shop while working at equipment | Physical 4 x 4 x 3 = 48 High | n/a | Mark lines on the floor to designate the work space. Schedule work to avoid overcrowding. | n/a | ( YES ( NO |
|  | contact with persons or objects being moved within the shop | Physical 4 x 4 x 3 = 48 High | n/a | Mark lines on the floor to designate work space. Schedule work to avoid overcrowding. | n/a | ( YES ( NO |
|  | electrical hazards associated with damaged cords, damaged operating controls, or access to service disconnects and breakers | Physical 4 x 4 x 3 = 48 High | n/a | Tag and remove defective tools/equipment from service. | n/a | ( YES ( NO |
|  | electrical hazard from servicing equipment that has hazardous energy that has not been locked out/tagged out or brought to “zero” energy state | Physical 4 x 4 x 3 = 48 High | n/a | Tag and remove defective tools/equipment from service. | n/a | ( YES ( NO |
|  | fall down steps fall when accessing dust collector for maintenance | Physical 4 x 4 x 3 = 48 High |  | Follow good housekeeping practices. Use handrails, keep steps free and clear of trip and slip hazards, avoid carrying materials that obstruct view of path of travel. work within work platform on dust collector | n/a | ( YES ( NO |
|  | fire risk resulting from friction (nails or metal in machined wood) | Physical 4 x 4 x 3 = 48 High | n/a | Post location of fire extinguishers and evacuation procedures. | n/a | ( YES ( NO |
|  | material stored that may tip or fall and strike a person | Physical 4 x 4 x 3 = 48 High | n/a | Keep materials stored in such a manner that they will not tip or fall and strike a person. | n/a | ( YES ( NO |
|  | noise exposure when equipment is operating | Physical 4 x 4 x 3 = 48 High | n/a | n/a | hearing protection | ( YES ( NO |
|  | working at heights (roof construction projects) | Physical 4 x 4 x 3 = 48 High | n/a | Always have someone holding the ladder. Have a fall protection plan in place if working at heights greater than 3 m. | fall protection (anchor point, lanyard, and full body harness) | ( YES ( NO |
| Psycho-social Exposure | bullying and verbal harassment with adults and students | Psychosocial 1 x 4 x 1 = 4 Low | n/a | Follow visitor procedures. Follow working alone procedures for school staff (including security and door locking procedures). Follow safe and secure school procedures. | n/a | ( YES ( NO |

© Calgary Board of Education