CTS TMT—MEC OCCUPATIONAL HAZARD ASSESSMENT AND CONTROL

Note 1: Alberta’s Occupational Health and Safety Code (OH&S Code) provides specific compliance requirements. This document is meant as a summary or checklists to assist staff comply with the legislation or applicable school jurisdiction administrative policies and regulations.

Note 2: The employee is required to conduct a pre-job hazard assessment before commencing work.

Note 3: This is a general worksite hazard assessment. Depending on the school/instructional area/specific courses taught, some incidents/hazards may or may not be present.

| RISK ANALYSIS (A x B x C = DEGREE OF RISK) |
| --- |
| A Frequency of Exposure to Hazard | B Incident/Hazard Probability | C Potential Consequence | Degree of Risk | Risk Classification |
| 1 = Less than once a month 2 = At least once a month 3 = At least once a week 4 = One or more times daily | 1 = Not likely 2 = Remote: not likely by once every 5–20 yrs 3 = Occasional: likely to happen once every 1–5 yrs 4 = Probable: expected to happen one or more times/year | 1 = Negligible (no injury, first aid) 2 = Marginal (medical aid, minor injury or illness) 3 = Critical (lost time injury, temp. disability) 4 = Catastrophic (serious injury or illness) | 1–11 12–31 32–64 | L – Low M – Medium H – High |

| POTENTIAL HAZARD | POTENTIAL HAZARD DESCRIPTION | RISK ANALYSIS (A x B x C = Degree of Risk) | SUMMARY OF EXISTING CONTROLS |
| --- | --- | --- | --- |
|  |  |  | ENGINEERING | ADMINISTRATIVE Alberta’s Occupational Health and Safety Codes (OH&S Code) applicable school jurisdiction administrative policies and regulations | PERSONAL PROTECTIVE EQUIPMENT (PPE) Personal Protective Equipment (PPE) appropriate for the work is both worn and CSA certified/approved where required. | CONTROL IN PLACE YES/NO |
| Biological Exposure | body fluid exposure from injuries | Biological 4 x 4 x 1 = 16 Medium | sink for handwashing first aid kit and supplies | Use universal precautions. Ensure that personnel are trained in first aid. Post emergency procedures. Identify and establish sanitary and safe housekeeping practices. Establish handwashing practices. | protective gloves (latex or nitrile disposable gloves) safety glasses, goggles | ( YES ( NO |
| Chemical Exposure | exposure to metal cleaners, battery acid, solvent-based paints and thinners | Chemical 4 x 4 x 3 = 48 High | eyewash station equipment in safe and proper working order ventilation system | Ensure WHMIS training is available. Provide up-to-date MSDS. Follow safe handling and storage information on labels or MSDS. Ensure regular cleaning and maintenance of ventilation system. Establish handwashing practices. | Welding goggles Welding helmet Protective gloves and leather apron | ( YES ( NO |
|  | exposure to carbon monoxide and other fumes/vapours from vehicle exhaust | Chemical 4 x 4 x 3 = 48 High | local exhaust ventilation and general ventilation within the shop (i.e., tail pipe connected to local ventilation) | Ensure WHMIS training is available. Provide up-to-date MSDS. Follow safe handling and storage information on labels or MSDS. Ensure regular cleaning and maintenance of ventilation system. Minimize vehicle running within shop area. | n/a | ( YES ( NO |
|  | exposure to fumes from welding/brazing | Chemical 4 x 4 x 3 = 48 High | local ventilation systems in welding areas portable local exhaust system when welding in general shop area | Ensure WHMIS training is available. Provide up-to-date MSDS. Follow safe handling and storage information on labels or MSDS. Ensure regular cleaning and maintenance of ventilation system. | n/a | ( YES ( NO |
|  | exposure to dust from grinding and sanding | Chemical 4 x 4 x 3 = 48 High | local exhaust system attached to hand grinders eyewash station | Minimize dry sweeping and, whenever possible, use vacuums with filters to clean up dust. Ensure regular cleaning and maintenance of ventilation system. | safety glasses or goggles | ( YES ( NO |
|  | exposure to sand blasting (parts cleaner) and cabinet | Chemical 4 x 4 x 3 = 48 High | eyewash station | Minimize dry sweeping and, whenever possible, use vacuums with filters to clean up dust. Ensure regular cleaning and maintenance of ventilation system. | safety glasses or goggles | ( YES ( NO |
|  | exposure to vapours from paints and thinners, fillers | Chemical 4 x 4 x 3 = 48 High | local and general ventilation spray booth | Ensure regular cleaning and maintenance of ventilation system. | respirator | ( YES ( NO |
|  | fire risk from flammable solvent-based paints and thinners | Chemical 4 x 4 x 3 = 48 High | spray booth ventilation | Ensure WHMIS training is available. Provide up-to-date MSDS. Follow safe handling and storage information on labels or MSDS. Ensure regular cleaning and maintenance of ventilation system. Store chemicals in a separate room and in fire-rated cabinets. | n/a | ( YES ( NO |
|  | explosion hazard from compressed gases | Chemical 4 x 4 x 3 = 48 High | compressed gases stored in trolley/secured to trolley flashback arrestor and reverse flow check valve local exhaust ventilation | Check hoses for leaks and replace damaged or leaking hoses. Test regulators on cylinders for leaks. The gas torch is to be used by trained staff only. Extra cylinders are securely stored in the vertical position with a protective cap covering the valve. Store chemicals in a separate room and in fire-rated cabinets. | n/a | ( YES ( NO |
| Ergonomic Exposure | lifting and moving awkward and/or heavy parts, equipment, and materials | Ergonomic 4 x 4 x 3 = 48 High | n/a | Provide training in proper lifting technique. Get help with heavy or awkward loads if a lifting aid is not available. Assess the load; bend your knees; grasp the load with a firm grip; hold the load close to your body; and lift with your legs, keeping your back straight. Use lifting and positioning aids to accommodate work posture. Store heavy objects at waist height. Try to use better designed work tools and workstations. Use tools with a weight counter-balancer. | Gloves safety boots (CSA approved) | ( YES ( NO |
|  | working in awkward positions for long periods of time | Ergonomic 4 x 4 x 3 = 48 High | n/a | Rotate jobs as frequently as possible. Avoid working in one position for long periods of time. Take frequent breaks to stretch. Minimize awkward postures. | n/a | ( YES ( NO |
|  | injury caused by repetitive motions | Ergonomic 4 x 4 x 3 = 48 High | n/a | Learn to recognize repetitive stress injuries. Ensure repetitive tasks are properly paced. Take regular breaks. | n/a | ( YES ( NO |
| Physical Exposure | confined space (e.g., autobody spray booth, if cleaning downdraft area below grade) | Physical 4 x 4 x 3 = 48 High | n/a | Be familiar with safe operating and maintenance requirements. Follow proper procedures for working in confined spaces. | n/a | ( YES ( NO |
|  | fire hazard and explosion hazard due to compressed-gas cylinders | Physical 4 x 4 x 3 = 48 High | reverse-flow check valves to prevent flashback | Compressed gases cylinders are stored and handled in carts (never on side). Regulators are tested for leaks. Store and protected against damage and secure against falling. | n/a | ( YES ( NO |
|  | contact with compressed air that may penetrate skin | Physical 4 x 4 x 3 = 48 High | nozzle with pressure relief holes | Do not use compressed air to clean clothing or skin. | n/a | ( YES ( NO |
|  | burns from hot surfaces metal splashes during welding, cutting handling hot tools and equipment | Physical 4 x 4 x 3 = 48 High | n/a | Maintain good housekeeping. | welding goggles (CSA approved) welding helmet protective gloves and clothing leather apron | ( YES ( NO |
|  | contact with portable and pedestal grinders that are improperly guarded or adjusted | Physical 4 x 4 x 3 = 48 High | pedestal grinder work rest adjusted properly (3 mm gap max) | Dress the pedestal grinder wheel regularly. | face shield | ( YES ( NO |
|  | contact with sharp edges and materials, auto parts | Physical 4 x 4 x 3 = 48 High | n/a | Cover sharp materials with tape or other protective material. | n/a | ( YES ( NO |
|  | entanglement in rotating machinery, parts, belts, and tools | Physical 4 x 4 x 3 = 48 High | equipment guards | Secure loose clothing, tie back long hair, and remove all jewellery. | protective gloves and clothing leather apron | ( YES ( NO |
|  | pinch points on equipment and/or machinery with V-belt drives (e.g., compressors) | Physical 4 x 4 x 3 = 48 High | equipment guards | Secure loose clothing, tie back long hair, and remove all jewellery. | n/a | ( YES ( NO |
|  | electrical shock from damaged or exposed connections, inadequate grounding, welding processes, worn or damaged cables/cords, lack of proper gloves, and working in wet conditions | Physical 4 x 4 x 3 = 48 High | n/a | Equipment that is being repaired and/or maintained is locked/tagged out (zero energy state). Tag and remove defective tools/equipment from use. Check electrical cords and cables for damage. Repair or replace damaged cords and cables. | gloves glasses with side shields face shield non-conductive footwear (high voltage) for welding hearing protection | ( YES ( NO |
|  | falling objects, including vehicles | Physical 4 x 4 x 3 = 48 High | n/a | Materials or vehicles that are elevated must be secured against falling. Make sure the hoist is rated to handle the load. Communicate with others when moving materials. Use safety stands whenever working underneath a vehicle. | n/a | ( YES ( NO |
|  | noise from grinding and certain types of welding | Physical 4 x 4 x 3 = 48 High | n/a | n/a | hearing protection | ( YES ( NO |
|  | fire and explosion from welding or cutting close to combustible materials or welding or cutting gases from poorly fitting and leaky hoses fire risk from flammable/combustible liquids and wastes (i.e., rags) | Physical 4 x 4 x 3 = 48 High | local ventilation fire extinguishers and evacuation procedures | Use flammable liquids and gases in well-ventilated areas. Secure and use the least toxic materials for both students and the environment. | leather gloves safety glasses leather apron | ( YES ( NO |
|  | slip hazard from vehicle fluids, spilled paints, or water trip hazards from cables, hoses, and debris | Physical 4 x 4 x 3 = 48 High | n/a | Use good housekeeping practices. Put away all tools, equipment, and materials in their proper storage areas. Clean up spills immediately. | n/a | ( YES ( NO |
|  | welding arc flash (UV light or infrared radiation) | Physical 4 x 4 x 3 = 48 High | n/a | Follow electrical safety procedures. Ensure cables are in good condition and are properly grounded. Avoid standing in water or on wet surfaces. Avoid wearing sweaty clothes. Turn the disconnect switch off before plugging in or unplugging the high-voltage input cable. Ensure welding equipment is correctly connected before using. Ensure that main power terminals are located inside welding machine cover; ensure terminals are accessible only with tools. Protect cables form damage. Never touch wire spool while the wire is being fed. | gloves glasses with side shields face shield non-conductive footwear (high voltage) for welding hearing protection | ( YES ( NO |
|  | fire hazards due to welding | Physical 4 x 4 x 3 = 48 High | n/a | Do not cut or use a torch to cut old paint containers/drums or containers that may have contained flammable liquids. | welding shields and/or welding glasses helmet clothing made for welding (i.e., resistant to spark, flame, and heat) non-conductive footwear | ( YES ( NO |
|  | unsafe vehicle (e.g., not road worthy, faulty brakes, leaking oil or gasoline) | Physical 4 x 4 x 3 = 48 High | n/a | Perform a circle check on any vehicle that is under power (brakes, leaks, or engine malfunction). Drive safely. Communicate movement of vehicles in/out of shop. Use safety stands. | n/a | ( YES ( NO |
|  | vibration from tools/equipment | Physical 4 x 4 x 3 = 48 High | vibration isolation suspension systems | Rotate jobs as often as possible. Take frequent rest periods. Reduce intensity and duration of exposure. Provide and document ongoing safety education and training, including mandatory equipment and tool orientation. | n/a | ( YES ( NO |
|  | falls from height | Physical 4 x 4 x 3 = 48 High | n/a | Use proper ladders when working at heights (three-point contact). | anchor point, lanyard, and full body harness | ( YES ( NO |
| Psycho-social Exposure | bullying and verbal harassment with adults and students | Psychosocial 1 x 4 x 1 = 4 Low | n/a | Follow visitor procedures. Follow working alone procedures for school staff (including security and door locking procedures). Follow safe and secure school procedures. | n/a | ( YES ( NO |

© Calgary Board of Education