|  | Fabrication Health & Safety Guidelines Do not enter the instructional area unless the instructor is present. Report all dangers, incidents, any damaged tools or equipment, unsafe working environments, or injuries immediately. Know what to do in an emergency! Know the evacuation procedures. Be familiar with the location and proper use of all emergency equipment in the shop, including fire extinguishers, power shutoff buttons, fire blankets, first aid kits, and eyewash stations. No horseplay—report unsafe acts! Think safety! Welding requires skill and attention; therefore, you must be present and alert. Do not work in the shop area if you are tired. Stop and rest. if you are rushed. Slow down. if you are under the influence of alcohol or drugs Respect yourself, others, the instructor, and the tools, equipment, and instructional area. Be aware of the risks your work may pose to others, especially when using hazardous tools, equipment, or materials (e.g., arc welders, compressed air, grinders, cleaners, etc.) If you feel unsafe about a particular activity, consult with your instructor before proceeding. Perform safety checks on yourself, surroundings, tools, equipment, or materials. Wear the appropriate personal protective equipment (PPE) for the task to prevent injury: safety glasses (CSA approved) worn at all times in the shop hearing protection (ear muffs and plugs) respirator required clear face shield shade 5 eye protection (goggles, glasses, shield) shade 10–12 eye protection (welder’s helmet) dry gauntlet gloves required protective clothing (100% cotton/leather/wool flame-resistant garment blend, welder’s cap on head, no pockets) steel-toed safety boots (CSA approved). High heels or open-toed sandals are not permitted. Eye protection, such as safety glasses or face shields, must be worn when there is a possibility that the eyes or face will be exposed to any flying objects, intense heat, harmful light (e.g., welding), or splashes from hazardous chemicals. Long hair, loose clothing, and jewellery must be secured or removed to prevent them from getting caught in machinery. Only cotton clothing is allowed beneath the welding protective clothing. Be sure your work area is well-organized, well-lit, and local and general ventilation is on. Prevent unnecessary strain or injury by working in a comfortable position. Identify, handle, store, or dispose of any hazardous materials using WHMIS regulations. Know the location of the SDS for the materials being used. Paints solvents, oils, and other flammable materials must be labelled and stored away from the instructional area. Compressed gas cylinders are stored in an upright, locked position with cylinder caps in place. Do not use any tools or equipment unless you have been properly trained and can demonstrate the safe use, operation, and shutdown procedures. Do not use any tools or equipment unless you have permission. Securely fasten tools, equipment, and materials to the work surface as needed All safety guards must be in place while operating tools or equipment. Disconnect power when setting up a machine for use (e.g., blade, drill bit, mixer blade, etc.). Never leave tools or equipment operating while unattended. Stay with the tool or equipment until all parts have stopped moving. Clean your area at the end of class, returning all tools, equipment, materials, projects, and PPE safely and securely to their proper storage locations. Keep the floor, work areas, and exits clear and free of obstructions. |  |
| --- | --- | --- |