| MDC: media, design & communication Arts |
| --- |
| Communications Technology |
| task | Print Screening |
| hazards | Potential Hazards | Possible Consequences |
| Physical | electrical strong light leaning on glass fire and explosion pressure washer system slips and trips heat and cold stress | burns smoke inhalation electric shock eye damage cuts bruising |
| Chemical | chemicals: citra paste, chroma wet, plastisol inks, red-coat flammable and combustible materials: citra paste, chroma wet | eye irritation skin irritation burns |
| Biological | bacteria/viruses blood body fluids | illness |
| Ergonomic | n/a | n/a |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Inspect required PPE and replace if required. Inspect room for ventilation. Report any hazards. Review WHMIS workplace labels. |
| Safe Work Procedure | Cautions |
| Put on all required PPE. Use hand, body, and eye protection. Avoid chemical contact with eyes or direct contact with skin. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions for equipment and for chemicals. Follow the school safety policy. Wipe up spills immediately. Clean the screen with citra paste. Rinse using a pressure washer system. Apply chroma wet to the print surface of the screen using a brush. Rinse thoroughly with clean water. Flood the screen with heavy water flow (not fine spray) for a uniform sheet of water over screen. Apply the CDF film (light sensitive) sheet. Press out any air bubbles. Place in the drying booth. Create a black and white image. Print onto a transparency sheet. Place the transparency and prepared screen onto the exposure unit. Apply red-coat. Apply plastisol inks. Heat seal. Do not let your hands come into contact with the platen or the dry mount press. Do not close the press on your hands. Dry mount with the heat setting prescribed by the teacher. When closing the platen of the dry mount press, be sure that the print and the mount are the only items under the platen. Turn off and unplug the press at the end of the process. Put away all tools, equipment, and materials in their proper storage areas. Clean the work area. Establish handwashing practices. | Store chemicals at or below eye level to prevent splashes to eyes if dropped. Do not breathe vapours. Avoid exposing chemicals to sparks or flames. Do not lean on or apply pressure to the glass of exposure unit. Keep hands out of the spray of the pressure washer system. Do not point pressure washer at anyone. Direct the pressure washer away from you. Close the lid before starting the exposure unit. Do not touch platen of the dry mount machine. Never test the temperature of the press by touching with your hand. Print the screen in a well-ventilated room. Situate emergency eyewash stations close to print screening area. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |