| NAT: NATURAL RESOURCES |
| --- |
| Agriculture |
| task | Using Long-Handled Tools (sod lifter, garden weasel, hoe, shovel, rake, spade, fork, edger) |
| hazards | Potential Hazards | Possible Consequences |
| Physical | lifting and handling loads repetitive motion slips, trips, and falls hitting rocks in soil loose handle grips | bruising pinching eye irritation muscle strain cuts and scrapes repetitive motion injuries |
| Chemical | n/a | n/a |
| Biological | allergens: plants/pollen bacteria/viruses blood body fluids fungi/moulds parasites sewage | respiratory problems skin irritation eye irritation allergy symptoms illness |
| Ergonomic | heavy loads bending and lifting high branches | muscle strain and soreness |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on all required PPE. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions. Follow the school safety policy. Complete the task using proper hand tools. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work, and make sure to clean up the work area and the tools when you are done. Establish handwashing practices. | Do not breathe vapours. Be careful with sharp tools. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |