| NAT: NATURAL RESOURCES |
| --- |
| Wildlife |
| task | Using a Handheld Ice Auger |
| hazards | Potential Hazards | Possible Consequences |
| Physical | lifting and handling loads repetitive motion slips, trips, and falls moving parts vibration sharp blade | musculoskeletal injuries contusions lacerations abrasions pinching puncture wounds |
| Chemical | cleaning agent, lubricant oil | chemical burns skin irritation lung damage headache dizziness loss of consciousness |
| Biological | bacteria/viruses blood body fluids | illness |
| Ergonomic | poor or awkward posture repetitive motion lack of muscular strength, endurance, flexibility, and/or balance vibration incorrect handle height for user | bodily injury |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. Read, understand, and follow the manufacturer's operating manual and safety decals on the equipment before operating the equipment. (Go to http://www.ccohs.ca for more information.) Inspect and tighten blade screws and all joints. Ensure that the blade is sharp. |
| Safe Work Procedure | Cautions |
| Put on all required PPE. Wear non-slip footwear. Secure loose clothing, and tie back long hair. Remove jewellery. Read and follow the manufacturer’s instructions, precautions, and directions. Follow the school safety policy. Set the handle to correct height for the user—that is, no higher than the user’s underarm when the blade is touching the ice. Uncover the blade. Rest the blade on the ice. Press down on the top knob of the handle with one arm close to the right shoulder if right-handed. While pressing down on the handle knob, use the other hand to turn the ice auger clockwise. Apply steady downward pressure. Once through the ice, turn the auger counterclockwise while pulling up on the handle. Cover the blade. Put away all tools, equipment, and materials in their proper storage areas. Clean the work area. Establish handwashing practices. | Always cover blade when not in use. Keep the blade sharpened. Secure the auger for transport. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |