| CLUSTER | TMT: TRADES, MANUFACTURING, AND TRANSPORTATION |
| --- | --- |
| OCCUPATION | Construction |
| HAZARD CONTROLS | MATERIALS—SOLID WOOD LUMBER (hard and soft) |
| Engineering Controls | Photodisc/Thinkstock |
| proper lumber storage racks Refer to the engineering controls for the specific tool being used. |  |
| Administrative Controls |  |
| Use higher grades (FAS, vertical grain) of lumber (fewer defects, less warp). Use domestic woods in place of exotics: domestic woods are less prone to the development of wood allergy. Refer to the administrative controls for the specific tool being used. Provide initial training to include a thorough review of hazards and accidents associated with the job. Follow the school safety policy. Provide and document ongoing safety education and training, including mandatory equipment and tool orientation. Outline the “imminent danger/right to refuse” procedures. Ensure hazard signs and tags are in place. Tag and remove defective tools from service. Ensure tools are used under competent supervision. Schedule work to avoid overcrowding. Ensure repetitive tasks are properly paced. Post important emergency telephone numbers and contacts. Post lockdown procedures. Post fire drill procedures. Establish handwashing practices. Locate the emergency electrical shut-off. Place a non-slip surface on the floor. Ensure fire extinguishers are strategically located and marked. Provide a first aid kit and supplies, including an eyewash station and biohazard disposal. Ensure that the master control panel and panel breakers are properly labelled. Provide an ergonomically appropriate work area. Ensure that correct lighting is available. Correctly place and maintain smoke detectors and heat sensors. Post relevant safety and health facts in the work area. Ensure that students wear safe attire: no loose clothing or jewellery should be worn. Ensure that long hair is tied back and/or secured under a hat. Ensure WHMIS training is available. Provide up-to-date MSDS. Instruct students on proper lifting techniques. Follow lock-out procedures for performing maintenance. |  |

| Personal Protective Equipment (PPE) |  |
| --- | --- |
| Refer to the PPE for the specific tool being used. safety glasses (CSA approved) hearing protection coveralls closed shoes |  |