| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using a Portable Circular Saw |
| hazards | Potential Hazards | Possible Consequences |
| Physical | flying objects electrical shock lifting and handling loads noise repetitive motion moving parts sharp blade vibration | bruising pinching cuts/amputations hearing impairment eye irritation and/or eye damage chronic pain |
| Chemical | wood dust human-made material particulates (e.g., lexan, polycarbonate, laminates, MDF, and plywood) | respiratory damage |
| Biological | bacteria/virus blood body fluids | illness |
| Ergonomic | lifting heavy stock materials lighting | bodily injury eye strain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. For example, check for electrical cord and switch damage. Inspect the material for knots, splits, warp, nails, staples, or other defects. Inspect PPE and replace if required. Report any hazards. Check that all guards are in place and working correctly. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions. Follow the school safety policy. Position and clamp the material on saw horses or similar supports. Adjust the saw base for 3 mm to 6 mm (⅛ in to ¼ in) blade protrusion through the material to be cut. Hold the saw firmly in two hands. Pull the power trigger. Feed the blade into the material, and complete the cut. Let go of the power trigger to turn the tool off, and wait for the blade to completely stop before putting the saw down. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Do not breathe in vapours or dust. Use a stable and comfortable stance. Do not stand in line with the cut. Always use two hands on the saw. Clamp the material before cutting. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |