| tmt: trades, manufacturing, and transportation |
| --- |
| mechanics |
| task | Using a Pneumatic Drill |
| hazards | Potential Hazards | Possible Consequences |
| Physical | eye hazards: chipping, grinding, flying metal or dirt fire and explosion lifting and handling loads excessive noise compressed air system repetitive motion slips, trips, and falls hot parts moving parts | death bruising pinching eye irritation and/or eye damage hearing impairment burns punctures chronic pain cancer |
| Chemical | n/a | n/a |
| Biological | allergens: fumes and gases bacteria/viruses blood body fluids | asthma or other allergy symptoms illness |
| Ergonomic | work surface height lifting repetitive work | bodily injury chronic pain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. Adjust the work surface height appropriately for the user. Check that the ventilation system is operational before starting to drill. |
| Safe Work Procedure | Cautions |
| Put on required PPE. Secure loose clothing, and tie back long hair. Use tools and equipment under competent supervision. Work in isolation behind a barrier to minimize exposure of others to harmful flying objects when necessary. Follow the manufacturer’s instructions. Follow the school safety policy. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | n/a |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |