| tmt: trades, manufacturing, and transportation |
| --- |
| mechanics |
| task | Using a Spray Booth |
| hazards | Potential Hazards | Possible Consequences |
| Physical | eye hazards: flying debris, fluid, or dirt fire and explosion compressed air system skin exposure to solvents repetitive motion slips, trips, and falls | death eye irritation and/or eye damage burns chronic pain cancer |
| Chemical | solvents, coolants, oil, clutch fluid, transmission fluid, grease, silicone, brake fluid, gasoline, battery acid, refrigerant inhalation of solvents in paints, paint thinners, and primers | asphyxiation chemical burns dizziness, loss of motor skills headache stomach pain skin rashes, cracking and bleeding skin irritated eyes, nose, and throat blindness destruction of kidneys or liver interference with nervous system irregular heart beat frostbite |
| Biological | allergens: fumes and gases bacteria/viruses blood body fluids | asthma or other allergy symptoms illness |
| Ergonomic | work surface height manual handling of, consumables lifting repetitive work | bodily injury chronic pain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. Adjust the work surface height appropriately for the user. Check that the ventilation system is operational before starting to paint. |
| Safe Work Procedure | Cautions |
| Put on required PPE. Secure loose clothing, and tie back long hair. Automotive processes produce hazardous fumes and gases. Minimize exposure to hazardous fumes and gases by having a full-respiratory protection program (OSHA). Work with solvents only where there is fresh air and/or ventilation system. Solvents cannot always be smelled. Use tools and equipment under competent supervision. Automotive repair requires skill and attention; therefore, you must be present and alert! Follow the manufacturer’s instructions. Follow the school safety policy. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | n/a |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |