| NAT: NATURAL RESOURCES |
| --- |
| Forestry |
| task | Using a Broadcast Seeder |
| hazards | Potential Hazards | Possible Consequences |
| Physical | lifting and handling loads (loading with seeds) repetitive motion slips, trips, and falls moving parts | musculoskeletal injuries contusions lacerations abrasions pinching bruising |
| Chemical | toxic materials, depending on what is being spread with the broadcast seeder | chemical burns skin irritation lung damage headache dizziness loss of consciousness |
| Biological | bacteria/viruses blood body fluids allergens | illness allergy reactions |
| Ergonomic | poor or awkward posture due to heavy loads repetitive motion lack of muscular strength and/or endurance handle height on push unit or height of crank on hand-held unit | musculoskeletal injuries |
| Psychological | fatigue stress | inattentiveness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Wear proper footwear. Secure loose clothing, and tie back long hair. Remove jewellery. Use tools and equipment under competent supervision. Follow the manufacturer’s instructions. Use tools and equipment under competent supervision. Follow the school safety policy. Adjust the strap for comfort if using a hand-held unit. Keep your wrist as straight as possible while cranking a hand-held unit. Do not overload the unit. It should be comfortable to push (if using a push unit) or carry (if using a hand-held unit). Know the material you are spreading. Set the unit to the product’s delivery rate. Follow the recommended spreading pattern on product label. Try to walk at a steady pace. Always close the drop door of the seeder when not in motion or when not in use. Wash the spreader after each use. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | n/a |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |