| CLUSTER | TMT: TRADES, MANUFACTURING, AND TRANSPORTATION |
| --- | --- |
| OCCUPATION | Construction |
| HAZARD CONTROLS | EQUIPMENT—BAND SAW |
| Engineering Controls |  |
| dust extraction wheel enclosures magnetic motor starter switch blade guard(s) proper blade size and type for specific operation equipment securely fastened in place |  |
| Administrative Controls |  |
| Use a minimum 5-cm or 2-in margin of safety. Adjust the upper blade guide 5 mm or ¼ in above stock. Use a V-block for cutting round stock. Use relief cuts when cutting curves. Provide initial training to include a thorough review of hazards and accidents associated with the job. Follow the school safety policy. Provide and document ongoing safety education and training, including mandatory equipment and tool orientation. Outline the “imminent danger/right to refuse” procedures. Ensure hazard signs and tags are in place. Tag and remove defective tools from service. Ensure tools are used under competent supervision. Ensure the equipment is appropriate for the work to be done. Schedule work to avoid overcrowding. Ensure repetitive tasks are properly paced. Post important emergency telephone numbers and contacts. Post lockdown procedures. Post fire drill procedures. Establish handwashing practices. Locate the emergency electrical shut-off. Provide safe clearance for the equipment. Place a non-slip surface on the floor. Mark lines on the floor to designate the work space. Ensure fire extinguishers are strategically located and marked. Provide a first aid kit and supplies, including an eyewash station and biohazard disposal. Ensure that the master control panel and panel breakers are properly labelled. Keep the manufacturers’ manual for the equipment. Provide an ergonomically appropriate work area. Ensure that correct lighting is available. Correctly place and maintain smoke detectors and heat sensors. Post relevant safety and health facts in the work area. Ensure that students wear safe attire: no loose clothing or jewellery should be worn. Ensure that long hair is tied back and/or secured under a hat. Adhere to the Canadian Electrical Code during the operation, repair, and maintenance of equipment. Never leave the machine unattended. Adhere to OHS occupational exposure limits (OELs). Keep sharp tools sharpened. Post “high-voltage” signage. Follow lock-out procedures for performing maintenance. |  |
| Personal Protective Equipment (PPE) |  |
| impact-resistant safety glasses (CSA approved) hearing protection closed footwear |  |