| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using Abrasives |
| hazards | Potential Hazards | Possible Consequences |
| Physical | repetitive motion contact with material | repetitive motion injury abrasions |
| Chemical | wood dust poisons/toxins, including fibreglass, asbestos, and lead | respiratory damage |
| Biological | n/a | n/a |
| Ergonomic | n/a | n/a |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect the tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. Have unknown materials or surfaces lab tested for lead before sanding. |
| Safe Work Procedure | Cautions |
| Put on required PPE. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions. Follow the school safety policy. Position the material on the downdraft sanding table. Install abrasive on the chosen block or tool. Sand in an even and methodical pattern. Ensure all wood dust is contained at the work station and cleaned up when complete. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Do not breathe in vapours or dust. Do not sand unknown surfaces or materials, as old paint may contain lead. Use the correct size of abrasive for the tool. Paper discs should not protrude past the edges of the backing pad. Use the appropriate abrasive grit for the procedure. Refer to the MSDS for wood dust. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |