| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using Adhesives |
| hazards | Potential Hazards | Possible Consequences |
| Physical | skin bonding (cyanoacrylate glue) | skin damage |
| Chemical | polyurethane, cyanoacrylate ester, vinyl acetate polymers, epoxy resins Refer to the specific Material Safety Data Sheet for the product used. | skin irritation eye irritation respiratory irritation |
| Biological | n/a | n/a |
| Ergonomic | n/a | n/a |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Refer to the product label and the Material Safety Data Sheet (MSDS) for the specific product used. Inspect the tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. Check that the ventilation system is operational. |
| Safe Work Procedure | Cautions |
| Put on required PPE. Follow the manufacturer’s instructions. Follow the school safety policy. Secure loose clothing, and tie back long hair. Read the label and Material Safety Data Sheet (MSDS) for the specific product to be used. Provide adequate ventilation as required. Apply the adhesive to the material surface. Clamp the work as indicated in the product directions. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Do not breathe in vapours. Some two-part epoxies, once mixed, can spontaneously combust if left in a large quantity. Spread leftover epoxy thinly on waste material, and let it dry before disposal. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |