| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using a Disc/Belt Sanding Machine |
| hazards | Potential Hazards | Possible Consequences |
| Physical | flying objects electrical shock lifting and handling loads repetitive motion moving parts vibration | bruising pinching cuts, abrasions eye irritation and/or eye injury repetitive motion injury |
| Chemical | wood dust human-made material particulates (e.g., lexan, polycarbonate, laminates, MDF, and plywood) | respiratory damage |
| Biological | bacteria/virus blood body fluids | illness |
| Ergonomic | heavy stock materials lighting | bodily injury eye strain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect the tools, equipment, and materials for damage and other hazards. For example, check for electrical cord and switch damage. Inspect the material for knots, splits, warp, nails, staples, or other defects. Inspect PPE and replace if required. Report any hazards. Check that all guards are in place and working correctly. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions. Follow the school safety policy. Position the material on the machine table. Adjust the table angle. Turn the machine on. Push the material into the moving abrasive. Sand to the desired shape, maintaining a 5-cm or 2-in margin of safety. Use clamps if necessary. Round stock must be clamped in a V-block for sanding. Small and irregularly shaped pieces that cannot be held flat should also be clamped when sanding. Hold stock flat on the table. Turn the machine off, and wait for it to completely stop. Remove the material from the machine table. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Do not breathe in vapours or dust. Use a stable and comfortable stance. Use only the side of the sanding disc that is moving toward the table. Never sand pieces without a guide or supporting mechanism (table, mitre gauge, clamping jig). |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |