| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using Wood Finishes |
| hazards | Potential Hazards | Possible Consequences |
| Physical | fire | burns |
| Chemical | naptha, polyurethane, mineral spirits, petroleum distillates, linseed oil, varnish resin, tung oil (See the MSDS for the specific finish used.) volatile organic compounds | skin irritation eye irritation lung irritation headache nausea dizziness |
| Biological | n/a | n/a |
| Ergonomic | n/a | n/a |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Refer to the product label and the Material Safety Data Sheet (MSDS) for the specific product used. Inspect tools, equipment, and materials for damage and other hazards. Inspect the ventilation equipment. Inspect PPE and replace if required. Report any hazards. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions. Follow the school safety policy. Read the label and Material Safety Data Sheet (MSDS) for the specific product to be used. Ensure adequate ventilation as required. Apply the finish to the material surface using the desired method (e.g., wipe on, spray, brush). Dispose of finishing rags according to the product label and local fire department recommendations. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Do not breathe in vapours. Have a fire extinguisher available when using flammable finishes. Use only verified food-safe products for finishing projects that will be used for serving food or that are made for children. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |