| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using a Jointer |
| hazards | Potential Hazards | Possible Consequences |
| Physical | flying objects electrical shock lifting and handling loads noise repetitive motion moving parts sharp blade vibration | bruising pinching cuts/amputations hearing impairment eye irritation and/or eye damage chronic pain |
| Chemical | wood dust human-made material particulates (e.g., lexan, polycarbonate, laminates, MDF, and plywood) | respiratory damage |
| Biological | bacteria/virus blood body fluids | illness |
| Ergonomic | lifting heavy stock materials lighting | bodily injury eye strain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect the tools, equipment, and materials for damage and other hazards. For example, check for electrical cord and switch damage. Inspect the material for knots, splits, warp, nails, staples, or other defects. Inspect PPE and replace if required. Report any hazards. Check that all guards are in place and working correctly. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions. It is especially important to follow the manufacturer’s instructions for margin of safety when making a cut. Follow the school safety policy. Adjust the infeed table height to a maximum of 1.5 mm ( in) below the outfeed table for face jointing, or 3 mm (⅛ in) for edge jointing. Position the material on the machine infeed table. Adjust the fence to accommodate the width/thickness of your material but to minimize reaching over the unused cutter head. Adjust the guard to completely cover the cutter head under its spring action. Turn the machine on. Use push blocks or a two-handled push stick on the stock for face jointing or when edge jointing narrow stock. Feed the material over the cutter head, keeping the material flat against the table and fence. Complete the cut. (Note: A good rule of thumb is to maintain a 10-cm or 4-in margin of safety when completing the cut; however, manufacturer’s instructions may vary.) Always use a push block or push stick when you cannot maintain the minimum margin of safety using your hands alone! Hold the stock flat on the table when face jointing or flat against the fence when edge jointing. Remove the material from the outfeed table once you’ve pushed it completely past the guarded cutter head. Repeat the jointing process until a smooth, true surface is achieved. Turn the machine off, and wait for the cutter head to completely stop. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Do not breathe in vapours or dust. Use a stable and comfortable stance. Use a minimum 12-in material length. Be aware of the grain run-out direction. Feed the stock so that the cutter head is not going to tear the run-out grain. Always use push blocks or a two-handled push stick when face jointing or edge jointing a narrow board (e.g., when you cannot maintain the minimum margin of safety using your hands alone). Focus your attention on finger positioning! Never put your fingers at the back end of a board being face jointed or a narrow board being edge jointed. Hold the stock flat on the table when face jointing or flat against the fence when edge jointing. Specialized procedures, such as jointing a bevel, should be performed by the teacher or by the student only after satisfactory training and teacher supervision. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |