| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using a Pneumatic Nailer or Nail Gun |
| hazards | Potential Hazards | Possible Consequences |
| Physical | flying objects electrical shock noise lifting and handling loads repetitive motion moving parts vibration | bruising pinching cuts/piercing hearing impairment eye irritation and/or eye damage chronic pain |
| Chemical | n/a | n/a |
| Biological | bacteria/virus blood body fluids | illness |
| Ergonomic | lifting heavy stock materials lighting | bodily injury eye strain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. For example, check for electrical cord and switch damage. Inspect the material for knots, splits, warp, nails, staples, or other defects. Inspect PPE and replace if required. Report any hazards. Check that all guards are in place and working correctly. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions. Follow the school safety policy. Position and hold or clamp the material in a way that you cannot be hit by a deflected nail. This is especially important when nailing along an edge. Adjust the pressure for the material type and thickness. Hold the tool firmly. Push the safety tip against the material. Pull the trigger to fire the nail or brad. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Use a stable and comfortable stance. Use an air regulator to ensure the manufacturer’s recommended air pressure is used. Never point the nailer at yourself or others. Do not carry the tool with the trigger pulled. Bumping the safety tip will result in the discharge of a nail. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |