| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using Portable Power Tools |
| hazards | Potential Hazards | Possible Consequences |
| Physical | flying objects electrical shock lifting and handling loads repetitive motion moving parts vibration | bruising pinching cuts/amputations eye irritation and/or eye injury chronic pain |
| Chemical | wood dust human-made material particulates (e.g., lexan, polycarbonate, laminates, MDF, and plywood) | respiratory damage |
| Biological | bacteria/virus blood body fluids | illness |
| Ergonomic | lifting heavy stock materials lighting | bodily injury eye strain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. For example, check for electrical cord and switch damage. Inspect the material for knots, splits, warp, nails, staples, or other defects. Inspect PPE and replace if required. Report any hazards. Check that all guards are in place and working correctly. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions. Follow the school safety policy. Position and clamp the material. Adjust the speeds and angles for the specific operation. Hold the tool firmly in two hands. Pull the power trigger. Feed the bit or blade into the material and complete the action. Let go of the power trigger to turn the tool off, and wait for the bit or blade to completely stop before putting the tool down. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Do not breathe in vapours or dust. Use a stable and comfortable stance. Use two hands on the tool. Clamp or secure the material before cutting. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |