| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using a Portable Router |
| hazards | Potential Hazards | Possible Consequences |
| Physical | flying objects electrical shock lifting and handling loads noise repetitive motion moving parts vibration | bruising pinching cuts/amputations hearing impairment eye irritation and/or eye damage chronic pain |
| Chemical | wood dust human-made material particulates (e.g., MDF and plywood) | respiratory damage |
| Biological | bacteria/virus blood body fluids | illness |
| Ergonomic | lifting heavy stock materials lighting | bodily injury eye strain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. For example, check for electrical cord and switch damage. Inspect the material for knots, splits, warp, nails, staples, or other defects. Inspect PPE and replace if required. Report any hazards. Check that all guards are in place and working correctly. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions. Follow the school safety policy. Position and clamp the material on the work table. Adjust the guide fence and template, or use an edge bit with a guide bearing. Install the appropriate router bit (with the router unplugged). Adjust the router base for the desired depth of cut. Always use two hands on the router, and hold the router firmly with its base on the material and its bit clear of the cut. Use successive passes with increasing bit depth, when possible, until the final depth is achieved. Turn the router on. Feed the bit into the material against the direction of bit rotation and complete the cut. Cut against the direction of bit rotation. Turn the tool off and wait for the bit to completely stop before removing it from the material and putting the tool down. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Do not breathe in vapours or dust. Use a stable and comfortable stance. Install the router bit with ¾ of its shank buried in the collet, but do not bottom out the bit before tightening. Unplug the router when changing bits, when making adjustments, or when the router is not in use. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |