| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using a Router Table |
| hazards | Potential Hazards | Possible Consequences |
| Physical | flying objects electrical lifting and handling loads noise repetitive motion moving parts vibration | bruising, pinching cuts/amputations hearing impairment eye irritation and/or eye damage electrical shock chronic pain |
| Chemical | wood dust human-made material particulates (e.g., MDF and plywood) | respiratory damage |
| Biological | n/a | n/a |
| Ergonomic | lifting heavy stock materials lighting | bodily injury eye strain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. For example, check for electrical cord and switch damage. Inspect the material for knots, splits, warp, nails, staples, or other defects. Inspect PPE and replace if required. Report any hazards. Check that all guards are in place and working correctly. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions. Follow the school safety policy. Position the material on the machine table. Adjust the fence. Adjust the bit guard to ¼ in above the material. Turn the machine on. Feed the material into the bit against the direction of the bit rotation (conventional cut) and complete the cut, maintaining a 10-cm or 4-in margin of safety. Use a push stick if necessary. Use clamping/holding jigs for routing small parts. Hold the stock flat on the table and against the fence, mitre gauge, or template post. Turn the machine off, and wait for the bit to completely stop. Remove the material from the router table. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Do not breathe in vapours or dust. Use a stable and comfortable stance. Never trap material between the bit and the fence. Feed the material against the direction of bit rotation (conventional cut). Feeding with the direction of the bit rotation (climb cut) will result in kickback. Never position your fingers in line with the bit. Specialized procedures should be performed by the teacher or by the student only after satisfactory training and with teacher supervision. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |