| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using Sheet Goods |
| hazards | Potential Hazards | Possible Consequences |
| Physical | lifting and handling loads | bruising pinching |
| Chemical | Refer to the MSDS for the specific sheet stock used. wood dust, formaldehyde | respiratory illness eye irritation |
| Biological | n/a | n/a |
| Ergonomic | lifting and moving heavy and large materials | bodily injury |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Refer to the product label and Material Safety Data Sheet for the specific product used. Inspect tools, equipment, and materials for damage and other hazards. Inspect ventilation equipment. Inspect PPE and replace if required. Report any hazards. |
| Safe Work Procedure | Cautions |
| Put on required PPE. Follow the school safety policy. Refer to the safe work procedure for the tool or equipment to be used and the specific operation. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | When lifting sheet goods, use leg and arm muscles (not back muscles) and seek assistance when the weight is unreasonable for one person. Keep sheet goods stacked and stored neatly so that the sheet goods do not project into shop pathways. Use a cart or trolley for transporting large/heavy sheet stock. |

REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help.