| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Construction |
| task | Using a Thickness Planer |
| hazards | Potential Hazards | Possible Consequences |
| Physical | flying objects electrical lifting and handling loads noise repetitive motion moving parts sharp blade vibration | bruising pinching cuts/amputations hearing loss eye irritation and/or eye damage electrical shock chronic pain |
| Chemical | wood dust human-made material particulates (e.g., lexan, polycarbonate, laminates, MDF, and plywood) | respiratory damage |
| Biological | bacteria/virus blood body fluids | illness |
| Ergonomic | lifting heavy stock materials lighting | bodily injury eye strain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. For example, check for electrical cord and switch damage. Inspect the material for knots, splits, warp, nails, staples, or other defects. Inspect PPE and replace if required. Report any hazards. Check that all guards are in place and working correctly. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Secure loose clothing, and tie back hair. Follow the manufacturer’s instructions. Follow the school safety policy. Position the material (with at least one flat face) on the machine infeed table with a flat face down. Adjust the table or cutter head height, depending on the type of machine. Turn the machine on. Feed the material into the infeed side of the planer. Support long boards until they are halfway through the planer. Receive the material from the outfeed table. Readjust the table/cutter head height, and repeat until the desired thickness is achieved. Remove equal amounts of wood from both faces to minimize warp. Turn the machine off, and wait for the blade to completely stop. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Do not breathe in vapours or dust. Use a stable and comfortable stance. Do not reach past the ends of the infeed or outfeed tables or into the machine. Stock must be longer than the distance between the feed rollers. Do not look into the planer while it is running. Stand clear of the ejection path of the material. Be aware of the grain run-out. Feed the stock so that the cutter head will not tear run-out grain. Never attempt to plane across the grain; however, planing at an angle to the grain can minimize tear-out. Jamming or a slow feed rate often indicates dull knives. Sharpen and reset the knives. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |