| CLUSTER | TMT: TRADES, MANUFACTURING, AND TRANSPORTATION |
| --- | --- |
| OCCUPATION | Electro-Technologies |
| HAZARD CONTROLS | EQUIPMENT—PROGRAMMABLE LOGIC CONTROLLER (PLC) |
| Engineering Controls | Hemera/Thinkstock |
| fused power supply |  |
| Administrative Controls |  |
| Ensure the instruction and demonstration of use and safe practices. Follow all manufacturer’s safety instructions and guides. Keep the work area clean and tidy at all times. Follow the school safety policy. Provide and document ongoing safety education and training, including mandatory equipment and tool orientation. Outline the “imminent danger/right to refuse” procedures. Ensure hazard signs and tags are in place. Tag and remove defective equipment from service. Ensure equipment is used under competent supervision. Ensure the equipment is appropriate for the work to be done. Schedule work to avoid overcrowding. Ensure repetitive tasks are properly paced. Post important emergency telephone numbers and contacts. Post lockdown procedures. Post fire drill procedures. Establish handwashing practices. Locate the emergency electrical shut-off. Provide safe clearance for the equipment. Place a non-slip surface on the floor. Mark lines on the floor to designate the work space. Ensure fire extinguishers are strategically located and marked. Provide a first aid kit and supplies, including an eyewash station and biohazard disposal. Ensure that the master control panel and panel breakers are properly labelled. Provide an ergonomically appropriate work area. Ensure that correct lighting is available. Correctly place and maintain smoke detectors and heat sensors. Post relevant safety and health facts in the work area. Ensure that students wear safe attire: no loose clothing or jewellery should be worn. Ensure that long hair is tied back and/or secured under a hat. Prevent extension cords from becoming trip hazards or overhead distractions in high-traffic areas. Adhere to the Canadian Electrical Code during the operation, repair, and maintenance of equipment. Post “high-voltage” signage. Follow lock-out procedures for performing maintenance. |  |
| Personal Protective Equipment (PPE) |  |
| safety glasses or goggles (CSA approved) |  |