| Task hazard analysis |
| --- |
| Electro-Technologies |
| task | Using a Folding Knife |
| hazards | Potential Hazards | Possible Consequences |
| Physical | sharp edges | cuts and puncture wounds |
| Chemical | n/a | n/a |
| Biological | bacteria/viruses blood body fluids | Where others have touched devices, possible contamination via viruses/bacteria may occur. |
| Ergonomic | handle and blade rigidity | cuts and puncture wounds |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Report any hazards. Keep the knife clean and sharp. |
| Safe Work Procedure | Cautions |
| Use tools and equipment under competent supervision. Secure loose clothing, and tie back long hair. Follow the manufacturer’s instructions. Follow the school safety policy. Open the knife. Test for the blade for sharpness. Use correct techniques as per instruction and demonstrations. Clean and close knife on completion of work. Put away all tools, equipment, and materials in their proper storage areas. Clean the work area. Establish handwashing practices. | Do not use a dull knife as it may lead to poor technique that could cause cuts or puncture wounds. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |