| Task hazard analysis |
| --- |
| Electro-Technologies |
| task | Using a Programmable Logic Controller |
| hazards | Potential Hazards | Possible Consequences |
| Physical | electrical moving parts | electrical shock burns bruising |
| Chemical | n/a | n/a |
| Biological | bacteria/viruses blood body fluids | Where others have touched devices, possible contamination via viruses/bacteria may occur. |
| Ergonomic | n/a | n/a |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. For example, check for electrical cord damage. Inspect PPE and replace if required. Be aware of locations and operation of general lab emergency stop buttons. Report any hazards. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Complete the schematic (ladder) diagrams and wiring diagrams before proceeding with lab. Have the diagrams approved by the instructor. Put on all required PPE. Secure loose clothing, and tie back long hair. Remove jewellery. Use tools and equipment under competent supervision. Follow the manufacturer’s instructions. Follow the school safety policy. Physically set up the required equipment. Electrically connect the required equipment according to wiring diagram. Program the PLC according to the schematic (ladder) diagram. Have the work checked by the instructor. Energize the work and note the results. De-energize the work. Put away all tools, equipment, and materials in their proper storage areas. Clean the work area. Establish handwashing practices. | Ensure all diagrams are approved by the instructor before proceeding with the actual wiring. Ensure the schematic (ladder) diagram is approved by the instructor before programming the PLC. Ensure the physical wiring is checked by the instructor before energizing. Ensure a fused power supply is used. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |