| Task hazard analysis |
| --- |
| Electro-Technologies |
| task | Using Various Meters |
| hazards | Potential Hazards | Possible Consequences |
| Physical | electrical | electrical shock burns |
| Chemical | n/a | n/a |
| Biological | bacteria/viruses blood body fluids | Where others have touched devices, possible contamination via viruses/bacteria may occur. |
| Ergonomic | n/a | n/a |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. For example, inspect meter leads. Report any hazards. |
| Safe Work Procedure | Cautions |
| Use tools and equipment under competent supervision. Follow the school safety policy. Place the leads in the correct jacks. De-energize the circuit to be tested. Follow the manufacturer’s instructions. Connect the meter according to the manufacturer’s instructions. Unless meter is auto-ranging, the ranges are finite. Generally, start on the highest range and work down. Make sure the maximum rating of the meter is not exceeded. Have the work inspected by the instructor before energizing. Energize the circuit and observe the digital read-out or the reading from the appropriate scale if the meter is analog. De-energize the circuit and disconnect the meter. Restore the circuit under “test.” Put away all tools, equipment, and materials in their proper storage areas. Clean the work area. Establish handwashing practices. | Make sure the circuit to be tested is de-energized before attempting to open the circuit to make connections. Make sure the maximum rating of the meter is not exceeded. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |