| Task hazard analysis |
| --- |
| Electro-Technologies |
| task | Using a Voltmeter |
| hazards | Potential Hazards | Possible Consequences |
| Physical | electrical | electrical shock burns |
| Chemical | n/a | n/a |
| Biological | bacteria/viruses blood body fluids | Where others have touched devices, possible contamination via viruses/bacteria may occur. |
| Ergonomic | n/a | n/a |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. For example, inspect meter leads. Report any hazards. |
| Safe Work Procedure | Cautions |
| Use tools and equipment under competent supervision. Follow the manufacturer’s instructions. Have the work inspected by the instructor before energizing for the first time. Follow the school safety policy. Place leads in correct voltmeter jacks: red is positive and black is negative. There is no polarity when measuring AC, but polarity must be observed when measuring DC. Unless voltmeter is auto-ranging, the ranges are finite. Start on the highest range and work down. The maximum rating of the voltmeter for any range must not be exceeded. The voltmeter is connected in parallel (with the load). Observe the digital read-out or the reading from the appropriate scale if the voltmeter is analog. Disconnect the voltmeter. Put away all tools, equipment, and materials in their proper storage areas. Clean the work area. Establish handwashing practices. | The maximum rating of the voltmeter for any range must not be exceeded. Use caution when connecting probes to circuitry. Always treat all circuitry as if it is alive, and keep fingers clear. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |