| CLUSTER | TMT: TRADES, MANUFACTURING, AND TRANSPORTATION |
| --- | --- |
| OCCUPATION | Fabrication |
| HAZARD CONTROLS | CONSUMABLE—WELDING GASES |
| Engineering Controls |  |
| appropriate guards ventilation system dust and fume extraction equipment |  |
| Administrative Controls |  |
| Provide initial training to include a thorough review of hazards and accidents associated with the job. Follow the school safety policy. Provide and document ongoing safety education and training, including mandatory equipment and tool orientation. Outline the “imminent danger/right to refuse” procedures. Ensure hazard signs and tags are in place. Tag and remove defective tools from service. Ensure tools are used under competent supervision. Ensure the tool is appropriate for the work to be done. Schedule work to avoid overcrowding. Ensure repetitive tasks are properly paced. Post important emergency telephone numbers and contacts. Post lockdown procedures. Post fire drill procedures. Establish handwashing practices. Locate the emergency electrical shut-off. Provide safe clearance for the equipment. Place a non-slip surface on the floor. Mark lines on the floor to designate the work space. Ensure fire extinguishers are strategically located and marked. Provide a first aid kit and supplies, including an eyewash station and biohazard disposal. Ensure that the master control panel and panel breakers are properly labelled. Keep the manufacturer’s manual for the tool. Provide an ergonomically appropriate work area. Ensure that correct lighting is available. Correctly place and maintain smoke detectors and heat sensors. Post relevant safety and health facts in the work area. Ensure that students wear safe attire: no loose clothing or jewellery should be worn. Ensure that long hair is tied back and/or secured under a hat. Follow lock-out procedures for performing maintenance. Ensure WHMIS training is available. Provide up-to-date MSDS. Prevent extension cords from becoming trip hazards or overhead distractions in high-traffic areas. Secure and use the least toxic and harmful substance for the student and the environment. Adhere to OHS occupational exposure limits (OELs). Adhere to the Canadian Electrical Code during the operation, repair, and maintenance of equipment. Instruct students on proper lifting techniques. Provide proper storage for consumables. |  |

| Personal Protective Equipment (PPE) |  |
| --- | --- |
| hearing protection clear face shield shade 5 eye protection shade 10–12 eye protection dry gauntlet gloves protective clothing welder’s cap steel-toed safety boots (CSA approved) |  |