| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Fabrication |
| task | Using an Anvil |
| hazards | Potential Hazards | Possible Consequences |
| Physical | lifting and handling loads excessive noise repetitive motion slips, trips, and falls hot materials and equipment | death bruising pinching eye irritation and/or eye damage hearing impairment burns bodily injury chronic pain repetitive motion injuries |
| Chemical | n/a | n/a |
| Biological | bacteria/viruses blood body fluids | illness |
| Ergonomic | work surface height manual handling of steel lifting repetitive work | bodily injury chronic pain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. Adjust the work surface height appropriately for the user. |
| Safe Work Procedure | Cautions |
| Put on required PPE. Secure loose clothing, and tie back long hair. Use tools and equipment under competent supervision. Work in isolation or behind a barrier to minimize exposure of others to harmful rays when necessary. Follow the manufacturer’s instructions. Follow the school safety policy. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | n/a |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |