| TMT: TRADES, MANUFACTURING, AND TRANSPORTATION |
| --- |
| Fabrication |
| task | Using a Bench Grinder/Benchtop Grinder |
| hazards | Potential Hazards | Possible Consequences |
| Physical | electrical shock eye hazards: chipping, grinding, flying metal or dirt fire and explosion lifting and handling loads excessive noise repetitive motion slips, trips, and falls hot parts moving parts | death bruising pinching eye irritation and/or eye damage hearing impairment burns cuts chronic pain cancer repetitive motion injuries |
| Chemical | fumes: aluminum, beryllium, cadmium oxides, chromium, copper, fluorides, iron oxide, lead, manganese, molybdenum, nickel, vanadium, zinc oxides gases: carbon monoxide, hydrogen fluoride, nitrogen oxide, ozone, phosphine organic vapours: aldehydes (such as formaldehyde), di-isocyanates, phosgene | Acute effects (occurring immediately or quickly) include metal fume fever; damage to the respiratory tract; sore and dry throat; chest pain; breathing difficulty; skin irritation; irritation of the eyes, nose, and throat; nausea; dermatitis; headache; dizziness; and muscular weakness. Chronic effects (appearing over time) include kidney damage; emphysema; cancer; bone and joint problems; excess fluid in the lungs; siderosis; chronic effects to the nervous system, kidneys, digestive system, and mental capacity; lead poisoning; bronchitis; retinitis; pneumonia; and asphyxiation. oxygen deficiency death |
| Biological | allergens: fumes and gases bacteria/viruses blood body fluids | asthma or other allergy symptoms illness |
| Ergonomic | lifting repetitive work work surface height lighting | bodily injury chronic pain eye strain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |

| Pre-operational Safety Checks |
| --- |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. For example, inspect the material for defects. Check for electrical cord and switch damage. Inspect PPE and replace if required. Report any hazards. Check that all guards are in place and working correctly. Adjust the work surface height appropriately for the user. |
| Safe Work Procedure | Cautions |
| Put on required PPE. Secure loose clothing, and tie back long hair. Use tools and equipment under competent supervision. A grinder requires skill and attention; therefore, you must be present and alert! Follow the manufacturer’s instructions. Follow the school safety policy. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | n/a |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |