| TMT: TRADES, MANUFACTURING, and TRANSPORTATION |
| --- |
| Fabrication |
| task | Using an Oxyacetylene Welding Manifold |
| hazards | Potential Hazards | Possible Consequences |
| Physical | fire and explosion lifting and handling loads repetitive motion | death bruising eye irritation and/or eye damage burns repetitive motion injuries chronic pain |
| Chemical | compressed-gas cylinders: acetylene, oxygen | burns death |
| Biological | n/a | n/a |
| Ergonomic | manual handling of tanks, consumables lifting repetitive work | bodily injury chronic pain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damages and other hazards. Ensure that flashback arrestors are installed. Inspect PPE and replace if required. Report any hazards. |

| Safe Work Procedure | Cautions |
| --- | --- |
| Put on required PPE. Secure loose clothing, and tie back long hair. Tanks must be moved and managed under direct instructor supervision. Work in isolation or behind a barrier to minimize exposure of others to harmful rays when necessary. Follow the manufacturer’s instructions in regards to storage and usage. Never weld or grind in the manifold area. Follow the school safety policy. Put away all tools, equipment, and materials in their proper storage areas. Empty tanks must be clearly marked “MT” or by ring on the neck. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | n/a |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |