| TMT: TRADES, MANUFACTURING, AND TRANSPORTATION |
| --- |
| Mechanics |
| task | Using an Air Blow Gun |
| hazards | Potential Hazards | Possible Consequences |
| Physical | eye hazards: flying debris, fluid, or dirt excessive noise compressed air system repetitive motion slips, trips, and falls moving parts | eye irritation and/or eye damage hearing impairment chronic pain bruising |
| Chemical | exposure to solvents | chemical burns skin irritation eye injury particle inhalation |
| Biological | allergens: fumes and gases bacteria/viruses blood body fluids | asthma or other allergy symptoms illness |
| Ergonomic | lifting repetitive work | bodily injury chronic pain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. |
| Safe Work Procedure | Cautions |
| Put on required PPE. Always wear eye protection when using air tools! Automotive processes produce hazardous fumes and gases. Minimize your exposure. Secure loose clothing, and tie back long hair. Use tools and equipment under competent supervision. Automotive repair requires skill and attention; therefore, you must be present and alert! Follow the manufacturer’s instructions. Follow the school safety policy. Put away all tools, equipment, and materials in proper their storage areas. Do not use the air blowgun to clean brake dust from brake components; the air blowgun will disperse the dust through the workshop. Do not use a high-pressure air blowgun to disperse liquid solvents or fuels. A low-pressure blowing action can help these volatile materials evaporate more quickly, but a high-pressure air jet could atomize the liquid, which forms a flammable mixture. Make sure to direct the exhaust of air tools away from yourself and others working in the area. Do not point the air blowgun at people. Never use the air blowgun to blow air over yourself or other people. Make sure that you understand and observe all legislative and personal safety procedures when carrying out tasks with blow guns. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | n/a |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |