| TMT: TRADES, MANUFACTURING, AND TRANSPORTATION |
| --- |
| Mechanics |
| task | Using a Flux Core Arc Welding Machine (FCAW) |
| hazards | Potential Hazards | Possible Consequences |
| Physical | electrical shock electric and magnetic field (EMF) interference eye hazards: ultraviolet radiation, flashes, “weld spatter,” chipping, grinding, flying metal or dirt fire and explosion excessive noise compressed-gas cylinders skin exposure to radiation heat stress (from wearing protective clothing and being subjected to heat from the welding process) repetitive motion hot metals, materials, and equipment moving parts confined spaces reduced line of sight for teacher due to harmful rays from welding process | death disruption of pacemaker and other implanted medical devices bruising pinching eye irritation and/or eye damage hearing impairment burns chronic pain cancer repetitive motion injuries |
| Chemical | fumes: aluminum, beryllium, cadmium oxides, chromium, copper, fluorides, iron oxide, lead, manganese, molybdenum, nickel, vanadium, zinc oxides gases: carbon monoxide, hydrogen fluoride, nitrogen oxide, oxygen deficiency, ozone organic vapours: aldehydes (such as formaldehyde), di-isocyanates, phosgene, phosphine compressed-gas cylinders: argon, carbon dioxide | Acute effects (appear quickly) include metal fume fever; damage to respiratory tract; sore and dry throat; chest pain; breathing difficulty; skin irritation; irritation of the eyes, nose, and throat; nausea; dermatitis; headache; dizziness; and muscular weakness. Chronic effects (appear over time) include kidney damage; emphysema; cancer; bone and joint problems; excess fluid in the lungs; siderosis; chronic effects to the nervous system, kidneys, digestive system, and mental capacity; lead poisoning; bronchitis; retinitis; pneumonia; and asphyxiation. oxygen deficiency death |
| Biological | allergens: fumes and gases bacteria/viruses blood body fluids | asthma or other allergy symptoms illness |
| Ergonomic | work surface height manual handling of tanks, consumables lifting repetitive work | bodily injury chronic pain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. Adjust the work surface height appropriately for the user. Check that the ventilation system is operational before starting to weld. |
| Safe Work Procedure | Cautions |
| Put on required PPE. All welding processes produce hazardous gases. Minimize exposure to hazardous gases. Secure loose clothing, and tie back long hair. Use tools and equipment under competent supervision. Welding requires skill and attention; therefore, you must be present and alert! Work in isolation or behind a barrier to minimize exposure of others to harmful rays when necessary. Follow the manufacturer’s instructions. Follow the school safety policy. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | n/a |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |