| tmt: trades, manufacturing, and transportation |
| --- |
| mechanics |
| task | Using a Portable Drill |
| hazards | Potential Hazards | Possible Consequences |
| Physical | electrical shock eye hazards: flying metal or dirt fire and explosion lifting and handling loads excessive noise repetitive motion hot parts moving parts | death bruising pinching eye irritation and/or eye damage hearing impairment burns cuts and/or punctures repetitive motion injuries chronic pain |
| Chemical | n/a | n/a |
| Biological | bacteria/viruses blood body fluids | illness |
| Ergonomic | work surface height lifting repetitive work | bodily injury chronic pain |
| Psychological | fatigue stress | anxiety inattentiveness poor morale increased illness |
| Pre-operational Safety Checks |
| Inspect the work area for hazards. Inspect tools, equipment, and materials for damage and other hazards. Inspect PPE and replace if required. Report any hazards. Adjust the work surface height appropriately for the user. |
| Safe Work Procedure | Cautions |
| Put on required PPE. Secure loose clothing, and tie back long hair. Use tools and equipment under competent supervision. Follow the manufacturer’s instructions. Follow the school safety policy. Drills can catch the material being worked on, causing the material to rotate freely and hit something or someone. Make sure the work piece is secured. Use the correct drill bit for the procedure. Old bits can wear out due to metal fatigue. Replace bits according to the manufacturer’s guidelines. Put away all tools, equipment, and materials in their proper storage areas. Keep your work area clean as you work and make sure to clean up when you are done. Establish handwashing practices. | Drill bits can break and fly off. The drill can slip and the bit can puncture or cut a person. Use caution. |
| REPORT ANY HAZARDOUS SITUATION IMMEDIATELY! If an emergency occurs while completing any task or the tool or equipment malfunctions, shut off the power immediately, follow the lock-out procedure, and get help. |